## Slide 1: Design of Large, Lightweight Highpower Rockets
Narcon 2021
Frank Burke

## Slide 3: Topics/Agenda
Background
Why design lighter?
Materials
Advantages and Disadvantages of using Foam materials
Design Considerations
Choosing subjects
Design, simulation and tradeoffs
Material testing and limitations
Construction
Finishing
Examples

## Slide 4: Background
Building and flying rockets for 45 years
Building and flying R/C aircraft for 35 years.
Designing with depron foam for 15 years
Started Dynasoar Rocketry in 2015 to design and manufacture unique R/C rocket glider kits
Successfully Built and flown more than a dozen 6” to 10” diameter semi-scale highpower rockets using depron foam as the primary construction material.

## Slide 5: Why design lighter?
Minimize size and cost of both motors and parachutes
Allows smaller fields with larger rockets
Reduced risk of personal/property damage in case of failure
Potential to fly under FAR-101 weights, no waiver required!
Reduced velocities/loading for specific flight profiles(Titan II/Dyna-Soar)

## Slide 6: Typical Highpower Construction Materials
Cardboard
  Typically Heavy for tubing sizes over 4”
  A LOC 60” 7.5” diameter tube weighs 3.75 pounds!
  Paper and cardboard for skins can add more weight than you think!
Fiberglass
  Can be light and thin but typically heavy
  Moderately expensive
Carbon Fiber
  Extremely strong but light
  Expensive
Plywood
  Heavy

## Slide 7: Advantages and Disadvantages of using foam materials
Advantages
  Lightweight
  Inexpensive
  Easy to shape and work
  Most construction with Cyano and contact type glues(fast curing)
Disadvantages
  Susceptible to hangar rash
  Not suitable for ultra harsh landing sites or those with brambles/sagebrush etc
  Limitations in paint types and brands.

## Slide 8: Advantages and Disadvantages of using Foam materials
Depron(Expanded polystyrene)
  Available In US currently from rcdepron.com
  3mm(flexible and formable), and 6mm Stiffer high quality flatness and finish
MPF(Model plane foam)(EPS)
  Thickness variations
  Surface waviness
  Finish different on both sides.
  Flexible
EPP(Expanded polypropolene)
  Flexible, dent resistant, heavier than EPS, coarse visible grain

## Slide 9: Design Targets I chose for my models
Targeting 5-6# rtf weight using 29mm H and I motors for flights from 700-1200’
Typical motors: H-97, H-115, H-135, H-128, H-180, I-200,I-205
  Long small diameter motors put weight more forward than short stubby motors. I-205 is ideal for this size model.
6”-10” diameter
5-9’ tall
5’ chute and chute bag
Altimeter deployment.
No additional fiberglass or carbon fiber reinforcing of the airframe (to reduce time, complexity, cost and weight)

## Slide 10: Good Subjects for this build method.
Small fins(Hellfire missile, Redstone Missile, Jupiter C)
Mid mounted fins(Pershing 1A, Falcon Missile)
Forward Fins(Titan II/Dyna-Soar)
Finless models that need clear fins for stability(Atlas or Titan II)

## Slide 11: Design, simulation and tradeoffs
Design your model for the largest motor you intend on flying.
Plan your construction technique, material, stringers, skin, fin construction, mounting, altimeter and parachute location.
Use a simulator tool for mass balancing like openrocket.
  Weigh components, place your objects, determine your CG required given your motor choices and how much nose weight will be needed.
  Adjust placement, size, construction, motors etc to come up with a buildable model with some margin.
  Use components scaled for the application/weight, don’t just use whatever the hardware store has, things add up, especially in the tail.

## Slide 12: Design, simulation and tradeoffs

## Slide 13: Material testing
8” diameter with 4 full depth 6mm depron stringers with 6mm depron centering rings spaced 8” apart with 29mm Aerotech cardboard motor tube core.
6mm depron rated at 21psi+ with 10% deformation
Test of 75# on partial structure @~19.5psi with no deformation
Should rate 150# on complete structure

## Slide 14: Reduce Weight where possible!
Drill holes in ply centering rings to lighten them
Drill holes in polycarbonate fin roots to lighten them
Use the lightest weight hardware, eye bolts, avoid quick links etc unless the model needs nose weight.

## Slide 15: Construction:
Use Aircraft construction, a built up model with internal structure and skin.
Use interlocking pieces(tab/slot) to align pieces and provide mechanical joints
Plan and pre-build fin boxes if needed.
Think about recovery and landing loads, decent rate, parachute size
Space your centering rings and longerons close enough to give sufficient support to your skin.
Make sure the skin bonds to the stringers and centering rings, this provides much of the stiffness.
Plan for sufficient fin stiffness to prevent flutter and landing damage.

## Slide 16: Construction
Centering rings with 6-8” spacing
Longerons full depth to the stuffer tube and half depth not touching the stuffer tube
Longerons are notched into the centering rings for strength and alignment
Stuffer tube is slipped into place and glued after the major structure is slotted together.
Extra longerons and extra centering rings are added on the seam line where the skin wraps or abuts meaning exact alignment when gluing is less critical.

## Slide 17: Construction: Adhesives
Epoxy
  heavy, strong, can be high temperature, sparingly used for motor retention, ply centering ring to stuffer tube/parachute tube mounting.
Contact cements(UHU POR or 3m-77)
  Good for laminating large areas of foam or applying skin
CA(Cyanoacrylate)
  Quick setting, can be thin or gap filling
  Strong, but most types will eat foam
  Good for stiffening/soaking cardboard/wood
  Allows fast construction

## Slide 18: Design Considerations: Stuffer Tube and Ply plates
29mm cardboard or pml tubing for motor mount and to act as a spine for the model.
1/8” ply plate at the bottom of the model for securing the fins and for motor retention and launch pad securing.
1/8” ply plate at the top of the model to glue to the parachute compartment and secure the recovery attachment point.
Full ply plate or partial plates at the the top of the fins to support them if needed.

## Slide 19: Design Considerations: Fin design, material and mounting
Polycarbonate, 1/16” or 3/32”
  Polycarbonate is very flexible and can be very useful in specific designs, but need to transfer landing stress to the centering rings and not the foam skin.
  Use hardwood strips on the ply centering rings on each side of the fin root to help locate and take the stress of landing(pseudo fin can)
  Need foam stringers on each side of the fins for the skin to attach to.
Laminated foam fin design
  Carbon fiber rods/strips can be laminated in between foam to reinforce them for stiffness and for landing protection.
  Good for models with very large fin areas.
  Expect that foam fins will always take some landing damage, scuffs, small crushing etc.
  use a foam fin box to mount and support the fins.

## Slide 20: Design Considerations: Rail button mounting
There is no body tube, you can’t just screw them to the body tube or use a T-nut.
Mount hardwood blocks to the top and bottom ply centering rings, you must be able to locate these after skinning the model.

## Slide 21: Design Considerations: Altimeter placement
Needs to be close enough to the parachute bay to minimize squib wiring
Needs to be accessible for arming on the pad
Helpful to be as far forward as possible to help with CG
I Mount the altimeter in a 38mm tube with 3/8” vent hole right underneath the upper ply plate.
Created access door in the model held in place with magnets, door has vent hole as well.
Altimeter is held in place with Velcro strap.
Squib wire goes into the 29mm stuffer tube and up into parachute bay.

## Slide 22: Design Considerations: Parachute compartment
Needs to be just big enough to hold required parachute and nomex/chute bag
Needs to withstand the ejection charge force.
pml tubing helps prevent zippering and adds weight in the front of the model.
Ply cap and coupler that the squib wire goes through seals the parachute bay for ejection.

## Slide 23: Design Considerations: Nose Weight
Minimize risk of nose cone hitting and damaging the model
Minimize the part of the model that ejects
Mount the nose weight to the sub-structure, not inside the nose cone if possible.

## Slide 24: Design Considerations: Skinning
Skin the model in large sections
Allow for the skin thickness when calculating the size of the sheets
Add extra stringers/centering rings to support butt joints between sheets/sections.
Add extra stringers on each side of the fins to support the skin when you cut fin slots.
The Fuselage must be skinned before mounting the fins and rail buttons
  You must plan ahead on locating and cutting fin slots and rail button locations after skinning.

## Slide 25: Design Consideratins: Finishing
Depron can be painted with a water based paint, or with testors/model master ENAMEL sprays directly.
I’ve also used self adhesive ORACAL vinyl trim to fully or partially wrap models. Once applied you can heat the vinyl with a hot hair dryer and press down into the foam with really sets it and adheres it. It adds strength and resistance to hangar rash as well.
For small non complex curve areas monokote trim can also work.

## Slide 26: Design Considerstaions: Launch Pad
These can launch on any rail pad, however the high mounted altimeter is sometimes hard to arm due to height of the pad.
I built a simple launch pad using 3” black plastic plumbing pipe with a steel blast plate.
This keeps the model low to the ground to allow arming the model altimeter without needing a ladder.
Long separation of rail buttons requires 10-12’ rail to give adequate guide time.

## Slide 27: Design Considerations: Airframe Cost
Foam cost ~$40(2 sheets 3mm for skin, 2 sheets 6mm for airframe.
PML parachute Tubes and coupler $20
29mm Tubing and coupler $12
retainer $27
1/8” birch aircraft 5 ply plywood $20
Hardware $7(eye bolt/washers and rail buttons)
Polycarbonate $20

## Slide 28: Design Studies
Fullscale Hellfire Missile using normal HPR components.
~64” long, 7.5” diameter, small fins, forward fins.
Using loc 7.5” tubing, fiberglass mosquito style nose cone, 38mm motor mount, ¼” birch ply and centering rings and nose weight meant ~18-20 pounds RTF using J570 or bigger.
Requires 7’ chute
7# nose weight
~1500’ altitude

## Slide 29: Lightweight Version
7” diameter foam airframe.
29mm stuffer tube, PML 4” by 14” parachute bay
One 54” chute
13 oz nose weight
Just the very tip of the nose ejects
  Balast is attached to the front parachute bay on the outside so nose is not heavy
  Avoids two part recovery
5# RTF with I205
1250’ altitude

## Slide 30: Design Studies
Titan II Missile using normal HPR components.
~72” long, 7.5” diameter, clear fins.
Using loc 7.5” tubing, nested traffic cones for nose cone, Chain link fence post cap for the tip.
38mm motor mount, ¼” birch ply and centering rings, 3/16” polycarbonate fins and nose weight meant 20 pounds RTF using J570 or bigger.
Required 7’ chute.
4# nose weight.
~1500’ altitude

## Slide 31: Lightweight Version
8” diameter foam airframe
29mm stuffer tube, PML 4” by 14” parachute bay
One 54” chute
No nose weight
5.5# weight RTF with I205
1250’ altitude

## Slide 32: Design Studies
Pershing 1A Missile using normal HPR components.
72” long, 7.5” diameter, 1/8” fiberglass fins
Using loc 7.5” tubing, fiberglass nose cone, 54mm motor mount, ¼” birch ply and centering rings, nose weight meant 20 pounds RTF using J570 or bigger.
Required one 7’ chute.
7# nose weight.
~1500’ altitude

## Slide 33: Lightweight Version
8” diameter foam airframe.
29mm stuffer tube, PML 4” by 14” parachute bay
One 54” chute
No nose weight
5.5# weight RTF with I205
1250’ altitude

## Slide 34: Stringers and centering rings

## Slide 35: Stuffer tube, parachute bay, altimeter pod

## Slide 36: Assembly

## Slide 37: Recovery attachment

## Slide 38: Fin Mounting

## Slide 39: Alternate fin mounting

## Slide 40: Altimeter bay

## Slide 42: Links:
https://www.rcdepron.com/
https://www.rocketryforum.com/threads/10-lightweight-atlas-missile.129159/
https://www.rocketryforum.com/threads/7-5-titan-ii-missile-2-versions.70242/
https://www.rocketryforum.com/threads/full-scale-hellfire-at-5-pounds.120317/
https://www.rocketryforum.com/threads/lightweight-large-pershing-1a.126713/
https://www.rcgroups.com/forums/member.php?u=118173